## Harmonic Plus Noise (HNM) Time line files
v1.0: 24.06.2009 – Oytun Türk (draft)

This document describes the details of HNM database representation in time line files. Specifically, the details of fields under:
 „Processing parameters“ → procHeader
and
„Datagrams zone“ → data
are covered. For additional information on time line files and MARY unit selection database format, please refer to „UnitDatabaseFormat.odt“

Section		Info	Type	Bytes	Comments
Mary Header		magic int 4 A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”. / version int 4 A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0. / fileType int 4 a unique identifier identifying the type of file we are looking at. For Time line files, this is “500”.
Processing parameters		procHeaderSize short 2 the size of the upcoming byte field [in bytes] / procHeader byte[] procHeaderSize a field of UTF-8 encoded characters indicating the nature of the timeline contents, including relevant processing parameters (such as FFT sizes, pre-emphasis coefficient etc.)
Data header		sampleRate int 4 the reference sampling rate to convert samples in seconds / numDatagrams long 8 the number of datagrams in the file / datagramsBytePos long 8 the position of the datagrams zone in the file, in bytes / timeIdxBytePos long 8 the position of the time index in the file, in bytes
Datagrams zone	For each datagram	duration long 8 the datagram duration [in samples] / datagramSize int 4 the datagram size [in bytes] / data byte[] datagramSize the data for this datagram
Index	numIdx int 4 the number of index fields / idxInterval int 4 the interval between index fields [in samples] / For each index field bytePtr long 8 the position [in bytes, from beginning of file] of the datagram coming on or just before the current index field / timePtr long 8 the time position [in samples] bof the datagram coming on or just before the current index field / prevBytePos long 8 the byte position of the last datagram in the file / prevTimePos long 8 the time position of the last datagram in the file

Remarks:
- the datagrams' duration parameter refers to the “window shift“ of the datagrams, not to a possible “window length“ related to some particular feature extraction method.
- the index is placed at the end of the file to allow for the possibility of appending new datagrams.

There are two noise models for HNMs:
1. Time-domain waveform which is the difference between the original signal and resynthesised harmonic part optionally highpass filtered at maximum frequency of voicing for each analysis speech frame.
2. LPC based noise model which is the result of driving LP filters estimated from the difference between the original signal and the resynthesised harmonic part with random noise. An optional highpass filter can be applied similar to the time-domain waveform case to remove frequency components below maximum frequency of voicing for each speech frame.

„Processing parameters“ → procHeader

Section	Info	Comments	Values/Value range	Default value
procHeader	noiseModel	Noise model	1=WAVEFORM, 2=LPC	1
	numFiltStages	Number of filtering stages to smooth out MWF curve	{0, 1, 2, 3, 4, 5} / 0: No smoothing	2
	medianFiltLen	Length of median filter for smoothing the MWF curve	{4, 8, 12, 16, 20}	12
	maFiltLen	Length of moving average filter for smoothing the MWF curve	{4, 8, 12, 16, 20}	12
	cumAmpTh	Cumulative amplitude threshold [linear scale] for harmonic band voicing detection. Decrease to increase max. freq. of voicing values.	[0.1, 10.0]	2
	maxAmpTh	Maximum amplitude threshold [in DB] for harmonic band voicing detection. Decrease to increase max. freq. of voicing values.	[0.0, 20.0]	13.0
	harmDevPercent	Percent deviation allowed for harmonic peak. Increase to increase max. freq. of voicing values.	[0.0, 100.0]	20.0
	sharpPeakAmpDiff	Minimum amplitude difference [in DB] to declare an isolated peak as harmonic. Decrease to increase max. freq. of voicing values.	[0.0, 20.0]	12
	minHarmonics	Minimum total harmonics allowed in voiced regions	[0, 100]	0
	maxHarmonics	Maximum total harmonics allowed in voiced regions	[minHarmonics, 100]	100
	minVoicedFreq	Minimum voiced frequency for voiced regions [in Hz]	[0.0, 0.5*samplingRate]	0.0
	maxVoicedFreq	Maximum voiced frequency for voiced regions [in Hz]	[minVoicedFreq, 0.5*samplingRate]	5000.0
	maxFreqVoicingFinalShift	Final amount of shift to be applied to the MWF curve [in Hz]	[0.0, 0.5*samplingRate-maxVoicedFreq]	0.0
	neighsPercent	Percentage of samples that the harmonic peak needs to be larger than within a band. Decrease to increase max. freq. of voicing values.	[0.0, 100.0]	50.0
	harmCepsOrder	Cepstrum order to represent harmonic amplitudes. Increase to obtain better match with actual harmonic values.	[8, 40]	24
	regCepWarpMethod	Warping method for regularized cepstrum estimation	1=POST_MEL, 2=PRE_BARK	1
	regCepsLambda	Regularization term for cepstrum estimation. Increase to obtain smoother spectral match for harmonic amplitudes. However, this reduces the match with the actual amplitudes.	[0.0, 0.1]	1.0e-5
	noiseLpOrder	Linear prediction order for LPC noise part	[8, 50]	18
	preCoefNoise	Pre-emphasis coefficient for linear prediction analysis of noise part	[0.0, 0.99]	0.97
	hpfBeforeNoiseAnalysis	Remove lowpass frequency residual after harmonic subtraction?	0=NO, / 1=YES	1
	harmNumPer	Total periods for harmonic analysis	[2.0, 4.0]	2
	hpfAfterNoiseSynth	Remove lowpass noise components after synthesis	0=NO, / 1=YES	1

„Datagrams zone“ → data:

CASE 1: TIME-DOMAIN WAVEFORM NOISE MODEL

Section		Info	Type	Bytes	Comments
For each datagram	data	f0	float	4	f0 value [in Hz] (0.0f for unvoiced frame)
		maxFreqVoicing	float	4	maximum frequency of voicing [in Hz] (0.0f for unvoiced frame)
		numHarmonics	int	4	number of complex harmonic amplitudes
		complexAmps	float[]	numHarmonics*2*4	real and imaginary part of each harmonic starting from the first and ending at [numHarmonics]th
		noiseWaveLen	int	4	noise waveform size [in bytes]
		noiseWave	float[]	noiseWaveLen*4	noise part waveform for this datagram

CASE 2: LPC-BASED NOISE MODEL

Section		Info	Type	Bytes	Comments
For each datagram	data	f0	float	4	f0 value [in Hz] (0.0f for unvoiced frame)
		maxFreqVoicing	float	4	maximum frequency of voicing [in Hz] (0.0f for unvoiced frame)
		numHarmonics	int	4	number of complex harmonic amplitudes
		complexAmps	float[]	numHarmonics*2*4	real and imaginary part of each harmonic starting from the first and ending at [numHarmonics]th
		lpGain	float	4	gain of linear prediction filter
		lpCoeffs	float[]	noiseLpOrder*4	linear prediction coefficients for the noise part. noiseLpOrder is specified in procHeader.