# Finite State Transducer File

This gives an overview of the finite state transducer file format. This format is used for storage of lexica.

Section	Info	Type	Bytes	Comments
Header	encodingNameSize	int	4	specifies the length (in byte) of the following encoding name
	encoding	byte[]	encNameSizee	a UTF-8 encoded String, representing the name of the encoding used for storing arc-labels
	overallBits	int	4	number of bits used to store per-arc information (not all sizes may be supported, standard is 32)
	offsetBits	int	4	number of bits used to store the offests of node arcs. This number is part of per arc information. (standard is 20)
	nrArcs	int	4	number of arcs
Arcs	arcs	byte[]	nrArcs * overallBits / 8	Every arc consists of overallBits bits, information is structured as follows: / - bit 0: indicating whether this arc is the last of a node (1) or not (0), i.e. whether next arcs belong to another node / - bits 1 to overallBits-(1+offsetBits): storing the id of the arc label id of this node, i.e. the input/output symbol information. / - bits (overallBits-offsetBits) to (overallBits-1): storing the offset of the first arc belonging to the node this arc is pointing to. / The first arcs are those of the start node. Arcs with the label id 0 are special and only indicate that the node they belong to (go out from) is a final state.
LabelInfo	nrLabels	int	4	stores the number of labels
	labelOffsets	short[]	2 * nrLabels	every two succeeding values store the offsets (in labelStrings) of the input and output strings for a labelId (i.e. the id is increased with every such pair)
	labelStrings	byte[]		Strings encoded in encoding, delimited by the values of labelOffsets, representing input or output symbols