# Structure of the MARY Unit database

v11, 27.03.09 Marc: Added DirectedGraph file description.
v10, 31.10.08 Marc: added generic properties section to CART.
v9, 30.10.08 Marc: modified CART file description for MARY 4.0
v8, 14.11.06 Marc: added a “Precomputed Join Cost file” section.
v7, 06.09.06	Sacha: revised the timeline spec after the implementation of a reader/writer for this format.
v6, 18.07.06	Sacha: corrected timeline spec against duplicate index interval.
v5, 10.07.06 Marc Schröder: Corrected Target feature file spec following Anna's comments.
v4, 07.07.06	Sacha Krstulović
v3, 07.07.06	Marc Schröder
v2, 05.07.06	Marc Schröder
v1, 04.07.06	Anna Hunecke
## Overview
The database consists of several files, each representing one conceptually independent type of information.
- Config file: voice.config – contains pointers to all relevant data and code files that need to be combined to make this voice work. Can also contain various configuration settings. This is a MARY .config file, i.e. text in key-value pairs.
- CART file: for each named unit type, a CART tree doing the pre-selection of candidate units for a given linguistic and/or acoustic target context. The leafs of the CARTs are index numbers in the list of units.
- Unit file: a list of units, in the order corresponding to the database “time line” (see below). Each unit has a time code marking its start position on the time line, as well as a duration.
- Target cost feature file: specification + data for the target cost features. The specification describes the meaning of the data entries; it is followed by one data entry per unit, i.e. the index numbers of the target features are the same as for the units.
- Join cost feature file: specification + data for the join cost features. The specification describes the meaning of the data entries; it is followed by one data entry per unit, i.e. the index numbers of the join features are the same as for the units.
- Time line files: a time line file contains detailed information about the original audio data; the units and their features are in a way an abstraction of this original audio data. The time code in the units allows for their location on all time lines for this database. Examples:
  - PCM waveform of the original audio data;
  - pitch-synchronous LPC coefficients + residual allowing the reconstruction of the audio signal;
  - encoded audio in different forms, e.g. using the Speex codec;
  - MFCC coefficients describing the audio signal (but not allowing for reconstruction);
  - a mapper locating the original audio file names on the time line, helping to find the original location of a bad unit (for debugging).
The following sections will specify each type of file in detail.
## Config file
(to be filled in)
## CART file
Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For CART files, this is “100”.
Properties		propStringLength	short	2
		propString	byte[]	propStringLength	a String representing a properties file, in ISO-8859-1 encoding as created by Properties.store(). This can be used to encode arbitrary key-value pairs.
feature definition (identical to Target Feature File, see below)		...	...	...	...
		numDecisionNodes	int	4	the number of decision nodes that will follow
for each decision node		featureNameIndex int 4 index of the feature name according to the feature definition above / nodeType int 4 one of the following: / 0=BinaryByteDecisionNode / 1=BinaryShortDecisionNode / 2=BinaryFloatDecisionNode / 3=ByteDecisionNode / 4=ShortDecisionNode / questionValue int/float 4 float in case of BinaryFloatDecisionNode; / index of feature value in case of BinaryByteDecisionNode or BinaryShortDecisionNode; number of child nodes to follow in case of ByteDecisionNode or ShortDecisionNode (in which case the number of children must be identical to the number of possible values of the feature given in featureNameIndex) / childNodeIDs int[] 4*numberOfChildren whereby numberOfChildren = 2 for BinaryByteDecisionNode, BinaryShortDecisionNode and BinaryFloatDecisionNode, and numberOfChildern = questionValue for ByteDecisionNode and ShortDecisionNode.
		number of leaf nodes	int	4
for each leaf node	leafNodeType int 4 type of leaf node, where / 0 = IntArrayLeafNode / 1 = FloatLeafNode / 2 = IntAndFloatArrayLeafNode / 3 = StringAndFloatLeafNode / 4 = FeatureVectorLeafNode / 5 = PdfLeafNode / for IntArrayLeafNode numData int 4 number of data points to follow / data int[] 4*numData / for FloatLeafNode stddev float 4 standard deviation / mean float 4 mean / for IntAndFloatArrayLeafNode and StringAndFloatLeafNode numData int 4 number of data pairs to follow / for each data pair intVal int 4 numData such data / floatVal float 4 / for FeatureVectorLeafNode numData int 4 number of data points to follow / data int[] 4*numData

## DirectedGraph file
Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For DirectedGraph files, this is “110”.
Properties		propStringLength	short	2
		propString	byte[]	propStringLength	a String representing a properties file, in ISO-8859-1 encoding as created by Properties.store(). This can be used to encode arbitrary key-value pairs.
feature definition (identical to Target Feature File, see below)		...	...	...	...
		numDecisionNodes	int	4	the number of decision nodes that will follow
for each decision node		featureNameIndex int 4 index of the feature name according to the feature definition above / nodeType int 4 one of the following: / 0=BinaryByteDecisionNode / 1=BinaryShortDecisionNode / 2=BinaryFloatDecisionNode / 3=ByteDecisionNode / 4=ShortDecisionNode / questionValue int/float 4 float in case of BinaryFloatDecisionNode; / index of feature value in case of BinaryByteDecisionNode or BinaryShortDecisionNode; number of child nodes to follow in case of ByteDecisionNode or ShortDecisionNode (in which case the number of children must be identical to the number of possible values of the feature given in featureNameIndex) / childNodeIDs int[] 4*numberOfChildren whereby numberOfChildren = 2 for BinaryByteDecisionNode, BinaryShortDecisionNode and BinaryFloatDecisionNode, and numberOfChildern = questionValue for ByteDecisionNode and ShortDecisionNode. / NB: childNodeIDs are structured data, see below.
		number of leaf nodes	int	4
for each leaf node	leafNodeType int 4 type of leaf node, where / 0 = IntArrayLeafNode / 1 = FloatLeafNode / 2 = IntAndFloatArrayLeafNode / 3 = StringAndFloatLeafNode / 4 = FeatureVectorLeafNode / 5 = PdfLeafNode / for IntArrayLeafNode numData int 4 number of data points to follow / data int[] 4*numData / for FloatLeafNode stddev float 4 standard deviation / mean float 4 mean / for IntAndFloatArrayLeafNode and StringAndFloatLeafNode numData int 4 number of data pairs to follow / for each data pair intVal int 4 numData such data / floatVal float 4 / for FeatureVectorLeafNode numData int 4 number of data points to follow / data int[] 4*numData
		number of directed graph nodes	int	4
for each directed graph node		leafChildNodeID int 4 childNodeIDs are structured data, see below. / decisionChildNodeID int 4 childNodeIDs are structured data, see below.

Child node IDs are structured as follows:
the highest two bits indicate the type of child node as follows:
0: leaf node
1: decision node
2: directed graph node
The remaining 30 bits contain the index number.
## Unit file

Section	Info	Type	Bytes	Comments
Header	magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
	version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0.
	fileType	int	4	a unique identifier identifying the type of file we are looking at. For Unit files, this is “200”.
Unit data	numberOfUnits	int	4
	sampleRate	int	4	the sample rate of the original wave files, e.g. 16000 or 44100. Time codes of units are expressed in number of samples, but can be converted to seconds by division through this sample rate.
for each Unit	startTime long 8 start position of this unit on the time line, in number of samples. / duration int 4 duration of this unit on the time line, in number of samples

## Target cost feature file

Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For Target feature files, this is “300” for phone feature files and “301” for halfphone feature files.
Target cost feature specification	numberOfByteValuedDiscreteFeatures int 4 the number of entries of this type; can be 0 This is useful for discrete features that have just a few different possible values. / for each byte-valued discrete feature for each value featureWeight float 4 / featureNameSize short 2 / featureName byte[] featureNameSize a UTF-8 encoded String, representing the feature name, e.g. “stress” / numberOfValues byte 1 number of possible string values for this feature; must be < 128. / valueSize short 2 / value byte[] valueSize a UTF-8 encoded String, representing one possible value of the current feature. In feature data entries, values will be identified by their index position in this list. / numberOfShortValuedDiscreteFeatures int 4 the number of entries of this type; can be 0. This can be used for discrete features that have many different possible values. / for each short-valued discrete feature for each value featureWeight float 4 / featureNameSize short 2 / featureName byte[] featureNameSize a UTF-8 encoded String, representing the feature name, e.g. “stress” / numberOfValues short 2 number of possible string values for this feature; must be < 16384. / valueSize short 2 / value byte[] valueSize a UTF-8 encoded String, representing one possible value of the current feature. In feature data entries, values will be identified by their index position in this list. / numberOfContinuousFeatures int 4 the number of entries of this type; can be 0. This can be used for continuous features, with a very high number of possible values. / for each continuous feature featureWeight float 4 / weightingFunctionSize short 2 if 0, a linear weighting function is assumed; else, the following string specifies a weighting function to use / weightingFunctionName byte[] weightingFunctionSize a UTF-8 encoded String, representing the name of the weighting function to use + optional arguments, e.g. “step 20%” would mean a step function costing 0 when the difference is less than 20%, and featureWeight when the difference is 20% or more. / featureNameSize short 2 / featureName byte[] featureNameSize a UTF-8 encoded String, representing the feature name, e.g. “unit_duration”
		numberOfUnits	int	4	number of rows in the upcoming array
target cost feature values, one for each unit		byte-valued discrete features byte[] numberOfByteValuedDiscreteFeatures / short-valued discrete features short[] 2*numberOfShortValuedDiscreteFeatures / continuous features float[] 4*numberOfContinuousFeatures

## Join cost feature file

Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For Join feature files, this is “400”.
Join cost feature specification	numberOfFeatures int 4 the number of join cost features / for each join cost feature featureWeight float 4 / weightingFunctionSize short 2 if 0, a linear weighting function is assumed; else, the following string specifies a weighting function to use / weightingFunctionName byte[] weightingFunctionSize a UTF-8 encoded String, representing the name of the weighting function to use + optional arguments, e.g. “step 20%” would mean a step function costing 0 when the difference is less than 20%, and featureWeight when the difference is 20% or more.
		numberOfUnits	int	4	number of rows in the upcoming array
join cost feature values, one for each unit		left join cost features float[] 4*numberOfFeatures / right join cost features float[] 4*numberOfFeatures

## Precomputed Join Cost file
This file provides a fast run-time access to join costs at diphone boundaries. Use in the run-time system is optional, but can increase run-time performance enormously (I hope).
For space reasons, the list of pre-computed joins is very sparsely filled; including all possible joins would make the file size explode. Joins are possible only between the left and right half-phone of the same phoneme; joins with costs above some threshold are considered impossible and are not listed.
That means, combinations of left and right halfphone units not occurring in this list are taken to be unjoinable.

This file will not be useful when diphones are missing and we need to fall back to half phones; in these rare events, we will still need to compute the join costs online; that means, we will still need a join cost feature file.

Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For precomputed Join cost files, this is “450”.
		numberOfLeftUnits	int	4
join cost section, one for each left unit	join cost, one for each right unit	left unit index int 4 / number of right units int 4 / right unit index int 4 / cost of joining the left and right units float 4

## Time line files

Section		Info	Type	Bytes	Comments
Mary Header		magic int 4 A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”. / version int 4 A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “40”, corresponding to MARY 4.0. / fileType int 4 a unique identifier identifying the type of file we are looking at. For Time line files, this is “500”.
Processing parameters		procHeaderSize short 2 the size of the upcoming byte field [in bytes] / procHeader byte[] procHeaderSize a field of UTF-8 encoded characters indicating the nature of the timeline contents, including relevant processing parameters (such as FFT sizes, pre-emphasis coefficient etc.)
Data header		sampleRate int 4 the reference sampling rate to convert samples in seconds / numDatagrams long 8 the number of datagrams in the file / datagramsBytePos long 8 the position of the datagrams zone in the file, in bytes / timeIdxBytePos long 8 the position of the time index in the file, in bytes
Datagrams zone	For each datagram	duration long 8 the datagram duration [in samples] / datagramSize int 4 the datagram size [in bytes] / data byte[] datagramSize the data for this datagram
Index	numIdx int 4 the number of index fields / idxInterval int 4 the interval between index fields [in samples] / For each index field bytePtr long 8 the position [in bytes, from beginning of file] of the datagram coming on or just before the current index field / timePtr long 8 the time position [in samples] bof the datagram coming on or just before the current index field / prevBytePos long 8 the byte position of the last datagram in the file / prevTimePos long 8 the time position of the last datagram in the file

Remarks:
- the datagrams' duration parameter refers to the “window shift“ of the datagrams, not to a possible “window length“ related to some particular feature extraction method.
- the index is placed at the end of the file to allow for the possibility of appending new datagrams.

## Definitions

Time measurement: every time will be measured with a couple of (long sampleIndex, int sampleRate).

Time-spacing mode: can be “REGULAR” for regularly spaced signal samples or vectors of coefficients resulting from fixed rate processing, or “VARIABLE” for vectors of variably-spaced coefficients (e.g., resulting from pitch-synchronous processing).

Datagram: a piece of timeline-related information, regardless of its time-spacing mode.

Break units: a non-phonetic/virtual type of unit, aimed at marking the position of the utterance boundaries (corresponding to the boundaries of the original wav files). Can be of two types, /BEGIN/ and /END/ (i.e., do include the begin unit at the beginning of a file, and the end unit at the end, even if there will be redundant /BEGIN//END/ couples among the units).