# Structure of the MARY Unit database

v1, 04.07.06	Anna Hunecke
v2, 05.07.06	Marc Schröder
v3, 07.07.06	Marc Schröder
v4, 07.07.06	Sacha Krstulović
v5, 10.07.06 Marc Schröder: Corrected Target feature file spec following Anna's comments.
v6, 18.07.06	Sacha: corrected timeline spec against duplicate index interval.
## Overview
The database consists of several files, each representing one conceptually independent type of information.
- Config file: voice.config – contains pointers to all relevant data and code files that need to be combined to make this voice work. Can also contain various configuration settings. This is a MARY .config file, i.e. text in key-value pairs.
- CART file: for each named unit type, a CART tree doing the pre-selection of candidate units for a given linguistic and/or acoustic target context. The leafs of the CARTs are index numbers in the list of units.
- Unit file: a list of units, in the order corresponding to the database “time line” (see below). Each unit has a time code marking its start position on the time line, as well as a duration.
- Target cost feature file: specification + data for the target cost features. The specification describes the meaning of the data entries; it is followed by one data entry per unit, i.e. the index numbers of the target features are the same as for the units.
- Join cost feature file: specification + data for the join cost features. The specification describes the meaning of the data entries; it is followed by one data entry per unit, i.e. the index numbers of the join features are the same as for the units.
- Time line files: a time line file contains detailed information about the original audio data; the units and their features are in a way an abstraction of this original audio data. The time code in the units allows for their location on all time lines for this database. Examples:
  - PCM waveform of the original audio data;
  - pitch-synchronous LPC coefficients + residual allowing the reconstruction of the audio signal;
  - encoded audio in different forms, e.g. using the Speex codec;
  - MFCC coefficients describing the audio signal (but not allowing for reconstruction);
  - a mapper locating the original audio file names on the time line, helping to find the original location of a bad unit (for debugging).
The following sections will specify each type of file in detail.
## Config file
(to be filled in)
## CART file
Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “1”.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For CART files, this is “1”.
CART data		numberOfCarts	int	4
for each CART	nameSize short 2 in bytes / name byte[] nameSize a UTF-8 encoded String / numberOfNodes int 4 / for each node nodeSize short 2 in bytes / node byte[] nodeSize a UTF-8 encoded String

The String representing the nodes is in the format inherited from FreeTTS. The only difference is that the list of numbers contained in leaf nodes are not the instance numbers of a unit type, but directly the index numbers of the unit in the unit list.
## Unit file

Section	Info	Type	Bytes	Comments
Header	magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
	version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “1”.
	fileType	int	4	a unique identifier identifying the type of file we are looking at. For Unit files, this is “2”.
Unit data	numberOfUnits	int	4
	sampleRate	int	4	the sample rate of the original wave files, e.g. 16000 or 44100. Time codes of units are expressed in number of samples, but can be converted to seconds by division through this sample rate.
for each Unit	startTime long 8 start position of this unit on the time line, in number of samples. / duration int 4 duration of this unit on the time line, in number of samples

## Target cost feature file

Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “1”.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For Target feature files, this is “3”.
Target cost feature specification	numberOfByteValuedDiscreteFeatures int 4 the number of entries of this type; can be 0 This is useful for discrete features that have just a few different possible values. / for each byte-valued discrete feature for each value featureWeight float 4 / featureNameSize short 2 / featureName byte[] featureNameSize a UTF-8 encoded String, representing the feature name, e.g. “R:SylStructure.parent.stress” / numberOfValues byte 1 number of possible string values for this feature; must be < 128. / valueSize short 2 / value byte[] valueSize a UTF-8 encoded String, representing one possible value of the current feature. In feature data entries, values will be identified by their index position in this list. / numberOfShortValuedDiscreteFeatures int 4 the number of entries of this type; can be 0. This can be used for discrete features that have many different possible values. / for each short-valued discrete feature for each value featureWeight float 4 / featureNameSize short 2 / featureName byte[] featureNameSize a UTF-8 encoded String, representing the feature name, e.g. “R:SylStructure.parent.stress” / numberOfValues short 2 number of possible string values for this feature; must be < 16384. / valueSize short 2 / value byte[] valueSize a UTF-8 encoded String, representing one possible value of the current feature. In feature data entries, values will be identified by their index position in this list. / numberOfContinuousFeatures int 4 the number of entries of this type; can be 0. This can be used for continuous features, with a very high number of possible values. / for each continuous feature featureWeight float 4 / weightingFunctionSize short 2 if 0, a linear weighting function is assumed; else, the following string specifies a weighting function to use / weightingFunctionName byte[] weightingFunctionSize a UTF-8 encoded String, representing the name of the weighting function to use + optional arguments, e.g. “step 20%” would mean a step function costing 0 when the difference is less than 20%, and featureWeight when the difference is 20% or more. / featureNameSize short 2 / featureName byte[] featureNameSize a UTF-8 encoded String, representing the feature name, e.g. “R:SylStructure.parent.stress”
		numberOfUnits	int	4	number of rows in the upcoming array
target cost feature values, one for each unit		byte-valued discrete features byte[] numberOfByteValuedDiscreteFeatures / short-valued discrete features short[] 2*numberOfShortValuedDiscreteFeatures / continuous features float[] 4*numberOfContinuousFeatures

## Join cost feature file

Section		Info	Type	Bytes	Comments
Header		magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
		version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “1”.
		fileType	int	4	a unique identifier identifying the type of file we are looking at. For Join feature files, this is “4”.
Join cost feature specification	numberOfFeatures int 4 the number of join cost features / for each join cost feature featureWeight float 4 / weightingFunctionSize short 2 if 0, a linear weighting function is assumed; else, the following string specifies a weighting function to use / weightingFunctionName byte[] weightingFunctionSize a UTF-8 encoded String, representing the name of the weighting function to use + optional arguments, e.g. “step 20%” would mean a step function costing 0 when the difference is less than 20%, and featureWeight when the difference is 20% or more.
		numberOfUnits	int	4	number of rows in the upcoming array
join cost feature values, one for each unit		left join cost features float[] 4*numberOfFeatures / right join cost features float[] 4*numberOfFeatures

## Time line files

Section	Info	Type	Bytes	Comments
Header	magic	int	4	A magic code identifying MARY database files; the integer value 0x4d415259, corresponding to the ASCII text “MARY”.
	version	int	4	A version number, as a quick way to check whether the database format is expected to be readable by a given code. For the current specification, this will be “1”.
	fileType	int	4	a unique identifier identifying the type of file we are looking at. For Time line files, this is “5”.
Processing parameters	procHeaderSize short 2 the size of the upcoming byte field [in bytes] / procHeader byte[] procHeaderSize a field of UTF-8 encoded characters indicating the nature of the timeline contents, including relevant processing parameters (such as FFT sizes, pre-emphasis coefficient etc.)
Data header	sampleRate	int	4	the reference sampling rate to convert samples in seconds
	numDatagrams	long	8	the number of datagrams in the file
	timeSpacingMode	byte	1	One of REGULAR (0) or VARIABLE (1)
Data				Depends on timeSpacingMode (see below.)

Two case arise for the data part, depending upon the timeSpacingMode:

REGULAR:

Section	Info	Type	Bytes	Comments
	datagramSize	int	4	the size of a datagram [in bytes]
	duration	long	8	the (fixed) time rate of the datagrams [in samples]
Data	datagrams	byte[]	numDatagrams*datagramSize	a series of fixed-size datagrams

VARIABLE:

Section		Info	Type	Bytes	Comments
Index	numIdx long 8 the number of index fields / idxInterval int 4 the interval between two index values [in samples] / For each index field begin long 8 the position [in bytes, from beginning of file] of the datagram nearest to the current index / offset long 8 the time difference [in samples] between the current index position and the nearest datagram position
Data	For each datagram	datagramSize int 4 the datagram size [in bytes] / duration long 8 the datagram shift [in samples] / datagram byte[] datagramSize one datagram (of variable-size)

Remark: the duration parameter refers to the “window shift“ of the datagrams, not to a possible “window length“ related to some particular feature extraction method.

Fig.1: illustration of the format in the two different time-spacing modes

## Note: sketch of the access method for the Time line files

datagramVec[] give_me( long timeLocation, long timeSpan, int reqSampleRate ) {

/* Open the file, check the version, skip the txt header,
read the sampleRate, numDatagrams and the time-spacing mode */

rateRatio = reqSampleRate / sampleRate;
if ( mode == REGULAR ) {
file.read( datagramSize, sizeof(int) );
file.read( duration, sizeof(long) );
// Read the whole vector in one go:
nDatagrams = floor( timeSpan * rateRatio / duration );
if ( nDatagrams > numDatagrams ) { nDatagrams = numDatagrams; }
beginByte = floor( timeLocation * rateRatio ) * datagramSize;
file.skip( beginByte );
file.read( datagramVec, nDatagrams*size );
}
else if ( mode == VARIABLE ) {
file.read( numIdx, sizeof(long) );
file.read( idxInterval, sizeof(int) );
// Locate the relevant index:
indexNow = floor( timeLocation * rateRatio ) / idxInterval;
//NB: this is an integer division.
indexByte = indexNow * 16;
file.skip( indexByte );
file.read( begin, sizeof(long) );
file.read( offset, sizeof(long) );
// Use the index to find the closest datagram:
file.seek( begin );
// Then start hopping/skipping to reach the requested timeLocation:
timeNow = offset;
file.read( datagramSize, sizeof(int) );
file.read( duration, sizeof(long) );
scaledTimeLocation = floor( timeLocation * rateRatio );
while ( ( timeNow < scaledTimeLocation ) && (!file.eof()) ) {
timeNow += duration;
file.skip( datagramSize );
file.read( datagramSize, sizeof(int) );
file.read( duration, sizeof(long) );
}
// Read the first relevant datagram:
file.read( data, datagramSize );
datagramVec.append( data );
// Continue hopping/reading to cover the requested timeSpan:
file.read( datagramSize, sizeof(int) );
file.read( duration, sizeof(long) );
scaledTimeEnd = floor( (timeLocation + timeSpan) * rateRatio );
while ( ( timeNow < scaledTimeEnd ) && (!file.eof()) ) {
timeNow += duration;
file.read( data, datagramSize );
datagramVec.append( data );
file.read( datagramSize, sizeof(int) );
file.read( duration, sizeof(long) );
}
}
else {
/* Exception: unknown timeSpacing mode */
}
}

## Definitions

Time measurement: every time will be measured with a couple of (long sampleIndex, int sampleRate).

Time-spacing mode: can be “REGULAR” for regularly spaced signal samples or vectors of coefficients resulting from fixed rate processing, or “VARIABLE” for vectors of variably-spaced coefficients (e.g., resulting from pitch-synchronous processing).

Datagram: a piece of timeline-related information, regardless of its time-spacing mode.

Break units: a non-phonetic/virtual type of unit, aimed at marking the position of the utterance boundaries (corresponding to the boundaries of the original wav files). Can be of two types, /BEGIN/ and /END/ (i.e., do include the begin unit at the beginning of a file, and the end unit at the end, even if there will be redundant /BEGIN//END/ couples among the units).